Coventry Caravan Site Conditions

(From February 2011)

Site Boundaries

1.	The boundaries of the site shall be clearly marked, for example by fences or hedges.  It is recommended that a 3-metre wide area should be kept clear within the inside of all boundaries.

Site Plan

2.	The site owner shall provide the Local Authority with a scale plan of the layout of the site within twenty-eight days from the date of any written request and at any time when significant alterations to the site layout are undertaken.  The cost of such plans shall be met by the licence holder.  The plan shall indicate the useable area of the site and shall show the position of:

a.	All caravans including their enclosure boundaries and all garages, sheds, covered stores, car ports, covered walkways and car parking spaces associated with them.  Each plot number should be clearly marked.

b.	All site buildings and other permanent structures.

c.	All roads and paths and their associated lighting.

d.	All fire points and fire hydrants.

e.	All publicly accessible telephones.

f.	All electrical distribution points.

g.	All compounds for the storage of liquefied petroleum gas.

h.	All cesspits, septic tanks and connections to the public sewerage system.

i.	All drainage runs and inspection chambers.

j.	All communal refuse stores.

Density and space between caravans

3.	Subject to the following variations, every caravan shall be not less than 6 metres (the separation distance) from any other caravan which is occupied separately and not less than 2 metres from a road or communal car park.  The point of measurement for porches is the exterior cladding of the caravan.

-       Where a caravan has retrospectively been fitted with cladding from Class 1 fire rated materials to its facing walls, then the separation distance between it and an adjacent caravan may be reduced to 5.25 metres.

-	Porches may protrude 1 metre into the separation distance and must not exceed 2 metres in length and 1 metre in depth. The porch must not exceed the height of the caravan. Where a porch is installed only one door may be permitted at that entrance to the home, either on the porch or on the home.

-	Eaves, drainpipes and bay windows may extend into the separation distance provided the total distance between the extremities of two facing caravans is not less than 5 metres, except where Class 1 fire rated materials have been fitted in which case the extension into the separation distance shall not exceed 4.25 metres.

-	Any ramps, verandas and stairs extending more than 1 metre into the separation distance shall be of non-combustible construction. There should be 4.5 a metre clear distance between any such structure and any adjacent caravan.

- A garage, car port, shed or a covered storage space shall be permitted between units only if it is of non-combustible construction (including non-combustible roof) and sufficient space is maintained around each unit  so as not to prejudice means of escape in case of fire.  Windows in such structures shall not face towards the units on either side.  For cars and boats between units, see standard (28).

- Fences and hedges forming the boundary between adjacent caravans should be a maximum of 1 metre high.

4.	The density shall be consistent with relevant health and safety standards and fire risk assessments. The gross density shall not exceed 50 caravans to the hectare, calculated on the basis of the useable area (i.e.  excluding lakes, roads, communal services and other areas unsuitable for the siting of caravans, etc) rather than the total site area.

Roads, gateways and footpaths and overhead cables

- Roads and footpaths shall be designed to provide adequate access for emergency vehicles.  (Detailed guidance on turning circles etc is available from fire authorities).  Roads of suitable material shall be provided and maintained so that no caravan standing is more than 50 metres from a road.  Caravans shall each be connected to a carriageway by a footpath with a hard surface.  Roads shall not be less then 3.7 metres wide, or, if they form part of a clearly-marked one way traffic system, 3 metres wide.  Gateways shall be a minimum of 3.1 metres wide and have a minimum height clearance of 3.7 metres.

Footpaths shall not be less than 0.9metres wide.  Roads and footpaths shall be suitably lit.  Emergency vehicle routes within the site shall be kept clear of obstruction at all times.

Hard standings

- Every caravan shall stand on a concrete hard-standing  sufficient to take the load placed upon it, which shall extend over the whole area occupied by the caravan placed upon it, and shall project a sufficient distance outwards from its entrance or entrances to enable occupants to enter and leave safely. Guidance for new bases are contained in industrial guidance by the National Park Homes Council.

Requirement to Comply with the Regulatory Reform (Fire Safety) Order 2005

- The site owner (unless it is a single unit site or solely occupied by a family) shall make available the latest version of the fire risk assessment carried out under the Regulatory Reform (Fire Safety) Order 2005 for inspection by residents and when demanded, a copy of the risk assessment shall be made available to the local authority.

Fire Points

8.	These shall be established so that no caravan or site building is more than 30 metres from a fire point.  They shall be housed in a weatherproof structure, easily accessible and clearly and conspicuously marked "FIRE POINT".

Fire Fighting Equipment

9.	Where water standpipes are provided and there is a water supply of sufficient pressure and flow to project a jet of water approximately 5 metres from the nozzle, such water standpipes shall be situated at each fire point.   There shall also be a reel that complies with current British Standard or European Standard, with a hose not less than 35 metres long, having a means of connection to a water standpipe (preferably a screw thread connection) with a water supply of sufficient pressure and terminating in a small hand control nozzle.  Hoses should be housed in a box painted red and marked "HOSE REEL".

10.	Where standpipes are not provided but there is a water supply of sufficient pressure and flow, fire hydrants shall be installed within 100 metres of every caravan standing.   Hydrants shall conform to British Standard 750

11.	Where standpipes are not provided or the water pressure or flow is not sufficient, each fire point shall be provided with either water extinguishers (2 x 9 litre) .

Fire Warning

12.	A means of raising the alarm in the event of a fire shall be provided at each fire point.  This could be by means of a manually operated sounder, e.g.  metal triangle with a striker, gong or hand operated siren.  The advice of the fire authority shall be sought on an appropriate system.

Maintenance and Testing of Fire Fighting Equipment

- Access to any fire fighting equipment or view of any fire warning signage shall not be obstructed or obscured.

- All alarm and fire fighting equipment shall be installed, tested and maintained in working order by a competent person and be available for inspection by, or on behalf of, the licensing authority or the Fire and Rescue Service.  A log book shall be kept to record all tests and any remedial action.

- All equipment susceptible to damage by frost shall be suitably protected.

Fire Notices

16.	A clearly written and conspicuous notice shall be provided and maintained at each fire point to indicate the action to be taken in case of fire and the location of the nearest telephone.  This notice shall include the following:

"On discovering a fire

i.	Ensure the caravan or site building involved is evacuated

ii.	Raise the alarm

iii	Call the fire brigade (the nearest telephone is sited ..............................)

It is in the interest of all occupiers of this site to be familiar with the above routine and the method of operating the fire alarm and fire fighting equipment."

Fire Hazards

17.	Long grass and vegetation shall be cut at frequent and regular intervals where necessary to prevent it becoming a fire hazard to caravans, buildings or other installations on the site.  Any such cuttings shall be removed from the vicinity of caravans.  The space beneath and between caravans shall not be used for the storage of combustible materials.

Supply & Storage of Gas etc

18.     Gas (including natural gas) and oil installations, and the storage of supplies shall meet current statutory requirements , relevant Standards and Codes of Practice.

Liquefied Petroleum Gas (LPG) cylinders must not be positioned or secured in such a way as to impede access or removal in the event of an emergency.

Add this information to appendix of procedure. Consider adding as notes to licence?

Storage of LPG must have regard to any amendments to appropriate legislation and guidance.

Electrical installations

19.	Sites shall be provided with an electricity supply sufficient in all respects to meet all reasonable demands of the caravans situated on them.

20.	The electrical network installations shall be subject to regulation under current relevant legislation and must be designed, installed, tested, inspected and maintained in accordance with the provisions of the current relevant statutory requirements.

21.	Any work on electrical installations and appliances shall be carried out only by persons who are competent to do the particular type of work being undertaken, in accordance with current relevant statutory requirements.  The installations shall be inspected periodically: under IEE Wiring Regulations, every year or such longer period (not exceeding 3 years) as is considered appropriate in each case.  When an installation is inspected, it shall be judged against the current regulations.

The inspector should, within 1 month of such an inspection issue an inspection certificate in the form prescribed in the IEE Wiring Regulations which shall be retained by the site operator and displayed, supplemented or replaced by subsequent certificates, with the site licence.  The cost of the inspection and report shall be met by the site operator or licence holder.

22.	Overhead cables must comply with the current statutory requirements. At the time of writing these are the Electricity safety Quality & Community regulations 2002 SI2002/2665 (ESQR). In general, cables should not overhang roads at less than 5.8metres, fully insulated cables not less than 3.8 metres. Cables within easy reach of a property must be fully insulated and protected from interference.

23.    If there are overhead electrical lines on the site, suitable warning notices shall be displayed at the entrances to the site and on supports for the line.  Where appropriate  particular attention shall be drawn to the danger of masts of yachts or dinghies contacting the line.

Water supply

24.	All parks shall be provided with a water supply in accordance with current legislation, regulations and relevant British standards. Any work undertaken on supplies and installation shall be carried out only by appropriately qualified persons.

Drainage, sanitation and washing facilities

25.	Satisfactory provision shall be made for foul drainage, either by connection to a public sewer or sewage treatment works or by discharging to a properly constructed septic tank or cesspool approved by the local authority.

Surface water drainage shall be provided where appropriate to avoid standing pools of water. All roads shall have adequate surface water/storm drainage.

26.	Each caravan shall have its own water supply and water closet.  Each caravan standing shall be provided with a connection to the foul drainage system.  The connection shall be capable of being made airtight when not in use.

27.	Every site and every hard standing shall be provided with an adequate drainage system for the complete and hygienic disposal of foul, rain and surface water from the site, buildings, caravans, roads and footpaths.

Refuse disposal

28.	Every caravan standing shall have an adequate number of suitable non-combustible refuse bins with close-fitting lids or plastic bags.  Arrangements shall be made for the bins to be emptied regularly.  Where communal refuse bins are also provided these shall be of similarly constructed and housed within a properly constructed bin store.

Parking

29.	One car only may be parked between adjoining caravans provided that the door to the caravan is not obstructed.  Suitably surfaced parking spaces shall be provided where necessary to meet the additional requirements of the occupants and their visitors.  Plastic or wooden boats shall not be parked between units.

Recreation space

30.	Where children live on the site, space equivalent to about one-tenth of the total area shall be allocated for children's games and/or other recreational purposes.  This provision will normally be necessary because of the limited space available round the caravans, but may be omitted where there are suitable alternative publicly provided recreational facilities which are readily accessible.

Flooding

31.  The site owner shall establish whether the site is at risk from flooding by referring to the Environment Agency's Flood Map. Where there is risk from flooding the site owner shall consult the Environment Agency for advice on the likelihood of flooding, the depths and velocities that might be expected, the availability of a warning service and on what appropriate measures to take.

Notices

32.	A suitable sign shall be prominently displayed at the site entrance indicating the name of the site, along with:-

33.	A copy of the site licence with its conditions

34.  (a) Details of the current name and address and telephone number of the licence holder and manager and emergency contact details

(b) A copy of the most recent periodic electrical inspection report.

(c) A copy of the site owner's certificate of public liability insurance.

(d) A copy of the local flood warning system and evacuation procedures, if appropriate.

(e) A copy of the fire risk assessment made for the site.

35.	Notices and a plan shall be displayed on the site setting out the action to be taken in the event of an emergency.  They shall show where the police, fire brigade, ambulance, and local doctors can be contacted, and the location of the nearest public telephone.

36.	All notices shall be suitably protected from the weather and displayed where possible out of the direct rays of the sun, preferably in areas lit by artificial lighting.